LOMO Astele SPOTTING SCOPES

USER’S GUIDE

Astele 60Zm, Astele 60LER

Astele 70Zm, Astele 70LER

|  | PLEASE READ CAREFULLY BEFORE USE AND SAVE FOR FUTURE REFERENCE |
| --- | --- |

“LOMO” and “Astele” are trademarks of LOMO America, Inc., Prospect Heights, Illinois.

© 2005 LOMO America, Inc. All Rights Reserved. Printed in the US.

Congratulations on your purchase of a LOMO Astele Spotting Scope. Your LOMO Astele Spotting Scope is rugged and durable and with reasonable care, it will provide you with many years of service. Assembly and operation of a LOMO Astele Spotting Scope is quick and simple.

|  | WARNING! Never use a Telescope or Spotting Scope to look at the Sun! Observing the Sun, even for the shortest fraction of a second, will cause irreversible damage to your eye as well as physical damage to the Telescope or Spotting Scope itself. |
| --- | --- |

1. LOMO Astele 60 Spotting Scopes

1. 1.  ASSEMBLY AND OPERATION

1)	Remove the dust cover from the opening at the rear of the Spotting Scope.

2)	Insert the eyepiece into the opening and tighten the set screw.

3)	Remove the lens cap on the front of the Scope.

4)	Attach the LOMO Astele 60 to any standard camera tripod via the 1/4x20 threaded hole on the bottom of the Scope.

5)	Focus by turning the large, knurled rubber ring located at the front of the Scope near the main lens.

6)	If glare from the sun reduces visibility, attach the sunshade (included) to the front of the Scope.

1.2. MAGNIFICATION

Fixed magnification models

Your LOMO Astele 60 Spotting Scope is designed to use any standard 1.25" diameter Telescope eyepiece. To determine the magnification of your LOMO Astele 60, divide the focal length of the LOMO Astele 60 (1168mm) by the focal length of the Telescope eyepiece. For instance, a 40mm eyepiece, when used with the LOMO Astele 60, will produce 29x and a 25mm eyepiece will produce 47x.

Zoom models

To change magnification, twist the eyepiece barrel to the desired setting. On the LOMO Astele 60, the zoom eyepiece delivers 48x at the 24mm setting, 73x at the 16mm setting and 146x at the 8mm setting.

Note: Always start with the lowest magnification - the 24mm mark on the eyepiece. This will make it easier to center a subject in the Spotting Scope. Once the subject has been located, zoom up in magnification as needed.

2. LOMO Astele 70 Spotting Scopes / Telescopes

2.1. ASSEMBLY AND OPERATION

1)	Remove the dust cover from the opening at the rear of the Spotting Scope/Telescope.

2)	Insert the diagonal prism and screw it's knurled ring to the threads on the back of the Spotting Scope/Telescope and tighten.

3)	Insert the eyepiece into the opening of the diagonal prism and tighten the set screw.

4)	Remove the lens cap on the front of the Spotting Scope/Telescope.

5)	Attach your LOMO Astele 70 to any standard camera tripod via the 1/4x20 threaded hole on the bottom of the Spotting Scope/Telescope.

6)	Focus by turning the small silver knob located on the back cover of the Spotting Scope/Telescope to the right of the eyepiece.

7)	If glare from the sun reduces visibility, attach the sunshade (included) to the front of the Scope.

2.2. MAGNIFICATION

Fixed magnification models

Your LOMO Astele 70 Spotting Scopes is designed to use any standard 1.25" diameter Telescope eyepiece. To determine the magnification of the LOMO Astele 70, divide the focal length of the LOMO Astele Spotting Scope (925mm for the 70) by the focal length of the Telescope eyepiece. For instance, a 40mm eyepiece, when used with the LOMO Astele 70, will produce 23x.

Zoom Models

To change magnification, twist the eyepiece barrel to the desired setting. On the LOMO Astele 70, the zoom eyepiece delivers 38x at the 24mm setting, 58x at the 16mm setting and 116x at the 8mm setting.

Note: Always start with the lowest magnification - the 24mm mark on the eyepiece. This will make it easier to center a subject in the Spotting Scope. Once the subject has been located, zoom up in magnification as needed.

2.3. CAMERA ADAPTER (Astele 70 only)

The LOMO Astele camera adapter is designed to be used with 35mm or digital SLR cameras (cameras with removable lenses). It is not designed for point and shoot cameras with non-removable lenses.

2.3.1. ASSEMBLY

1)	Remove the eyepiece from the diagonal.

2)	Remove the diagonal by unscrewing the knurled ring located where the diagonal is attached to the Spotting Scope/Telescope body.

3)	Attach the camera adapter by threading its knurled ring onto the threads at the back of the Spotting Scope/Telescope body.

4)	Remove the lens from your SLR and attach the SLR body to the T-ring now attached to the camera adapter.

5)	Thread a T-ring for your specific brand and model of SLR camera (not supplied, but available at OpticsPlanet.com or any camera store) onto the threads located at the rear of the camera adapter.

2.3.2. OPERATION

With camera attached, the LOMO Astele 70 becomes a 925mm, f/13.2 telephoto lens (17x). Meter light by changing shutter speed manually or by setting your camera on aperture priority if available. ASA 400 or higher film is recommended

2.4. MOUNT ADAPTER (LOMO Astele 70)

The LOMO Astele 70 is also packaged with an adapter for attachment to a LOMO German Equatorial Astronomy Mount. It is not necessary to use this accessory for other applications.

3. Warranty

Your LOMO Astele Scope is covered by a Limited Lifetime Warranty against defects in materials and workmanship. Your LOMO Astele Scopes are rugged and very durable, but if it should need repair or servicing, contact LOMO America, Inc. at 888-446-7842, info@lomoamerica.com or 15 E. Palatine Rd., Unit 104, Prospect Heights, IL 60070, USA.